## Slide 1: Ergonomics
By Dr. Rakesh Kumar
Moderator- Dr. PR Deshmukh
ERGONOMICS

## Slide 2: Framework
Introduction
History
What is Ergonomics
Ergonomics- a Multidisciplinary science
Human Engineering
Work Physiology
Occupational Biomechanics
Anthropometry
Workplace Contributing Factors
Work related injuries and diseases
Principles of ergonomics
Ergonomics Job Analysis Methods
Benefits of ergonomics
What Are Ergonomic Improvements?
Engineering Improvements
Administrative Improvements
Safety Gear
Examples of ergonomic improvements
References

## Slide 3: Introduction
Poor job design and workplace design is one of various occupational hazards
Large and increasing numbers of workers affected by poor work design
Increasing prevalence of health problems related to a lack of ergonomics at work
Ergonomics is an integral part of any advanced occupational health services
Notes: Many workers suffer from injuries and diseases that result from manual work and the increased mechanization of work.

## Slide 4: History
Ancient man made pebble tools and scoop from antelope bones
17th century- Bernardino Ramazinni wrote about work-related complaints in his book "De Morbis Artificum "
1857- Term‘Ergonomics’ was first coined by Wojciech Jastrzebowski
Early 19th century- Frederick W. Taylor was a pioneer of ergonomic approach
World war II- Prompted interest in human-machine interaction
1970 The Occupational Safety and Health Act of 1970 (U.S.)
Purpose to "assure so far as possible every working man and
woman a safe and healthful working conditions to preserve human resources.“
Institutes for occupational health and safety in India:
1. Central Labour Institute, Mumbai (1960)
2. National Institute of Occupational Health, Ahmedabad
Notes: Australopithecus Prometheus selected pebble tools and made scoops from antelope bones
Bernardino Ramazinni (1633-1714) wrote about work-related complaints (that he saw in his medical practice) in the 1713 supplement to his 1700 publication, "De Morbis Artificum (Diseases of Workers)."
Wojciech Jastrzebowski created the word ergonomics in 1857 in a philosophical narrative, "based upon the truths drawn from the Science of Nature" (Jastrzebowski, 1857).
Frederick W. Taylor was a pioneer of this approach and evaluated jobs to determine the "One Best Way" they could be performed. At Bethlehem Steel, Taylor dramatically increased worker production and wages in a shoveling task by matching the shovel with the type of material that was being moved (ashes, coal or ore).
Frank and Lillian Gilbreth made jobs more efficient and less fatiguing through time motion analysis and standardizing tools, materials and the job process. By applying this approach, the number of motions in bricklaying was reduced from 18 to 4.5 allowing bricklayers to increase their pace of laying bricks from 120 to 350 bricks per hour.
World War II prompted greater interest in human-machine interaction as the efficiency of sophisticated military equipment (i.e., airplanes) could be compromised by bad or confusing design. Design concepts of fitting the machine to the size of the soldier and logical/understandable control buttons evolved.
After World War II, the focus of concern expanded to include worker safety as well as productivity.

## Slide 5: What is Ergonomics
Ergo – from the Greek word meaning work
Nomos – from Greek word meaning natural laws
Definition:
Science and practice of designing jobs and workplaces to match the
capabilities and limitations of the human body. (OSHA, 2000)
i.e, Science of fitting the job to the person rather than making the person fit the job
Objective:
To improve the fit between the physical demands of the workplace
and the employees who perform the work
i.e, To achieve best mutual adjustment of man and his work for
improvement of human efficiency and well being
Notes: Definition. The scientific study (Greek - nomos) of human work (Greek - ergon).
• Strategy. Ergonomics considers the physical and mental capabilities and limits of the worker as he
or she interacts with tools, equipment, work methods, tasks, and the working environment.
• Goal. Reduce work-related musculoskeletal disorders (MSDs) by adapting the work to fit the person,
instead of forcing the person to adapt to the work.
• Principle. Since everything is designed for human use or consumption, human characteristics should
be considered at the beginning of the design process.
Proactive- recognizing, anticipating and reducing riskfactors at planning stage of work process.
Reactive – identifying riskfactors and problems asso with work place and controlling them

## Slide 6: Ergonomics- a multidisciplinary Science
Human Engineering - Study of the principles of mechanics and anatomy in relation to human movement
Work Physiology- Static or Dynamic work
Occupational Biomechanics – a disciplinary science which explains the characteristics of biological system of the human body in mechanical terms.
Anthropometry - Study of human body measurements.
Notes: Biomechanics is the study of the structural elements
of the human body in relation to how the body functions
and how much stress, acceleration, and impact it can
stand.

## Slide 7: Workplace Contributing Factors
Aspects of work tasks which can lead to fatigue, musculoskeletal disorder (MSD) symptoms and injuries, or other types of problems

## Slide 8
Physical/mental capability, preexisting conditions, etc
Noise, temperature, humidity etc
  Heavy, Frequent, or Awkward Lifting
  Pushing, Pulling or Carrying Loads
  Working in Awkward Postures
  Hand Intensive Work
  Repetitive motions
  Forceful exertions
  Vibration

## Slide 9: Work-related Injuries and Disorders
Work related muskulo-skeletal are most common
Also known as:
  Repetitive Strain or Stress Injury (RSI)
  Cumulative Trauma Disorder (CTD)
  Overuse Syndrome
Occupational disorders of the soft issues like muscles , tendons, ligaments, joints & nerves
Usually occur slowly over time due to repetitive injuries to the soft tissues and nervous system
Symptoms of WMSD:
Discomfort, Pain, Numbness, Tingling, Burning, Swelling, Tightness, loss of flexibility
Risk of injury depends upon:
Duration, Frequency & Intensity of exposure or combinations of risk factors

## Slide 10
Injuries | Common sites | Cause
Bursitis | knee, elbow, shoulder | Kneeling, pressure at the elbow, repetitive shoulder movements
Carpal tunnel syndrome | wrist | Repetitive work with a bent wrist. Use of vibrating tools.
Epicondylitis | Elbow | Repetitive work, often strenuous
Ganglion | Back of hand or wrist | Repetitive hand movement
Osteo-arthritis | Any joint | Awkward liftting, pulling, pushing
Tendonitis | Any site | Repetitive movements
Tenosynovitis | Any site | Repetitive movements, often nonstrenuous
Tension neck or shoulder | Neck or shoulders | Sustained awkward postures
Trigger finger | Fingers | Repetitive movements. Excessive gripping

## Slide 11: Basic Ergonomic Principles
Work activities should permit worker to adopt several different
healthy and safe postures.
Muscle forces should be done by the largest appropriate
muscle groups available
Work activities should be performed with joints at about
mid-point of their range of movements(esp. head, trunk,
upper limb)

## Slide 12: Ergonomics principles at Workstation
Consider ergonomic factors like head height, shoulder height, arm reach, elbow height, hand height, leg length, and hand and body size while designing a workstation
80-100 cm
frequently used
work area
Occasional work area
Usual work area
25 cm
50 cm

## Slide 13: Ergonomics principles during sitting position
Bending foreward
No wrist support
No foot rest
Back straight and supported
Wrist supported and straight
Foot supported

## Slide 14: Ergonomics principles at workstation

## Slide 15: Ergonomics principles during standing position
Do pelvic tilt intermittently
Keep a chair nearby for taking rest intermittently
Workstation should have footrest

## Slide 16
Foot-rest
Chair available
Pelvic tilt

## Slide 17: Ergonomics principles during using hand tools and controls
Poor control position
Good control position

## Slide 18: Ergonomics principles during heavy physical work
Stand close to objects and
feet slightly apart
Keep back straight
Use both hands and
grip with whole hand
Place feet in walking position
Take help of others

## Slide 19: To summarize the ergonomic principles…
Straight back rule
Workstation at the level of umbilicus
Arm space
Pelvic tilt
Center of gravity
Neutral Position
No window adjacent to work station

## Slide 20: Benefits of ergonomics
Reduced fatigue and discomfort
Helps to prevent injuries like MSDs
Improved quality of life
Improved comfort, morale and job satisfaction
Improved quality of work
Improved productivity and reduced workers’ compensation costs and employee turnover
Reduced sickness absenteeism
Notes: Involving workers enhance worker motivation and job satisfaction, adds problem solving capablities, greater acceptance of change and they have greater knowledge of work and organization.

## Slide 21: Ergonomics Job Hazard Analysis Methods
Consist of various techniques for taking a systematic look at jobs and work tasks
It breaks a job into its various tasks, describes them, measures and quantifies the ergonomics risk factors inherent in the task, identifies conditions contributing to the risk factors, and determines corrective measures
Help decide which jobs and specific tasks may contribute to problems
e.g, Ergonomics Awareness Checklist- simple
Others complex and sophisticated methods
Methods vary according to types of work activities they address. e.g, workstation design, types of work, work environment
Notes: Evidence of WMSDs- health and medical indicators- follow up of workers report, conducting sx surveys & periodic medical examn. 2. Identifying risk facors in job – screening jobs, performing job analyses & setting priorties
using questionairres, vedio and audiotape analysis

## Slide 22
Conduct an initial job review
List Hazardous Jobs
Conduct a Risk Analysis
Prioritize Hazardous Jobs
Describe the hazards in each step
Take ergonomic modification
Evaluate it for risk reduction
Steps:
Notes: Screening jo risk factors may involve 1. walk through observational survey 2. interview with workers and supervisors 3. use of check list for scoring job features

## Slide 25: What Are Ergonomic Improvements?
Definition: Changes made to improve the “fit”
between a job and the capabilities of the employees performing it
Three strategies :
• Engineering improvements
• Administrative improvements
• Safety gear or personal protective equipment(PPE)

## Slide 26: Engineering Improvements
Engineering improvements include rearranging
modifying, redesigning, or replacing:
• Workstations,
• Equipment,
• Tools,
• Packaging
Reduce or eliminate existing hazards
Most effective strategy
Best time is when new facilities, processes, or work procedures are being planned

## Slide 27: Administrative Improvements
Reduce exposure to the hazard by controlling behaviors through design of safety rules and safe work practices and procedures
Include changing work practices or the way work is organized
Require continual management and employee compliance to ensure that the new practices and policies are effective

## Slide 28: Administrative Improvement Options
1. Providing variety in jobs
2. Adjusting work schedules and work pace
3. Providing recovery time (i.e., muscle relaxation time)
4. Ensuring regular housekeeping and maintenance of work
spaces, tools, and equipment
5. Increase workforce & Reduce workload
6. Training in recognition of risk factors

## Slide 29: Safety Gear or Personal protective equipment
Provides a barrier between the worker and the hazard source
Reduces the duration, frequency, or intensity of exposure
Includes gloves, knee and elbow pads, respirators, ear plugs, safety goggles, , aprons, safety shoes, and hats

## Slide 30: Examples of ergonomic improvements
Use food quality tools
2. Wear antivibration
gloves
3. Lubricate tool
regularly
Put shock absorber in vechile
Use well designed seat in vechile

## Slide 31
Awkward forward bending
Intensive hand use
Job dissatisfaction
Repetitive movements
Forceful extension
Unsupported static posture

## Slide 32: References:
1. Your health and safety at work: A collection of modules. International Labor Organization.
2. Ergonomics – The study of work. OSHA:2000
3. Ergonomics guidelines for manual material handling. NIOSH publications; Colombia parkway:2007
4. Sutton SC. A guide to ergonomics.
5. Cohen A et al. Elements of ergonomics programme. NIOSH publications; Colombia parkway: 1997.
6. Park K. Park’s Textbook of Preventive and social medicine. 18th edition. Bannout publication; Jabalpur: 2006. p.658-9.
7. Internet: http://www.ergoweb.com

## Slide 33
THANK YOU